## Slide 1: Intravenous cannulation

## Slide 2: What is IV cannulation?
Intravenous cannulation is a technique in which a cannula is placed inside a vein to provide venous access.
Venous access allows:
  sampling of blood
  administration of IV fluids and medications,

## Slide 3: Cannula
This device is available in various
  gauges (16-24 G),
  lengths (25-44 mm),
  compositions, and
  designs.

## Slide 4: Cannula
Gauge Size
22 Gauge: 0.8 mm
20 Gauge: 1.0 mm
18 Gauge: 1.2 mm
16 Gauge: 1.7 mm

## Slide 5: Tips
Routinely, use the smallest size (largest gauge number) of catheter if possible to prevent damage to the vessel intima
In an emergency situation use a large size catheter to allow administration of large volumes of fluid quickly

## Slide 6: Tips
The superficial veins of the upper extremities are preferred to those of the lower extremities for peripheral venous access
  they interfere less with patient mobility and pose a lower risk for phlebitis.

## Slide 7: Tips
It is recommended to choose a straight portion of a vein to minimize the chance of hitting valves.
Use the patient’s non-dominant arm (if possible)
For prolonged courses of therapy, it is recommended to start distally and move proximally as distal catheters are replaced.

## Slide 8: Indication
Repeated blood sampling
Intravenous administration of
  IV fluids
  Medications
  Chemotherapy
  Nutritional support
  Blood or blood products administration
  Radiological contrast agents for computed tomography, magnetic resonance imaging, or nuclear imaging

## Slide 9: Contraindications
No absolute contraindications to intravenous cannulation exist
Avoid peripheral venous access in an injured, infected, or burned extremity if possible

## Slide 10: Equipment
Non-sterile gloves
Tourniquet
Antiseptic wipes
5-ml syringe
Sterile gauze
Cannula
Saline
Adhesive Plaster

## Slide 11: Before the procedure
Introduce yourself to the patient. Explain the procedure to the patient and gain informed consent to continue
Make sure there is adequate light and that the room is warm enough to encourage vasodilation
Make sure the patient is in a comfortable position and place a pillow or a rolled towel under the patient’s extended arm
The patient’s skin should be washed with soap and water if visibly dirty

## Slide 12: Before the procedure
If difficulty is encountered in finding an appropriate vein, one of the following techniques may be used:
  Inspection of the opposite extremity
  Opening and closing the fist
  Using gravity (holding the arm down)
  Gentle tapping or stroking of the site
  Applying heat (warm towel/pack)

## Slide 13: Technique
Apply tourniquet and select the appropriate vein
Apply an antiseptic solution with friction for 30-60 seconds, allow to air dry for up. Once cleaned, do not touch or re-palpate the skin
Remove the cannula from its packaging and remove the needle cover ensuring not to touch the needle
Stretch the skin distally and tell the patient to expect a sharp scratch

## Slide 14: Technique
Insert the needle, bevel upwards at about 30 degrees
Advance the needle until a flashback of blood is seen in the hub at the back of the cannula
Once this is seen, progress the entire cannula a further 2mm, then fix the needle, advancing the rest of the cannula into the vein

## Slide 15: Technique
Insert the needle, bevel upwards at about 30 degrees
Advance the needle until a flashback of blood is seen in the hub at the back of the cannula
Once this is seen, progress the entire cannula a further 2mm, then fix the needle, advancing the rest of the cannula into the vein

## Slide 16: Technique
Release the tourniquet, apply pressure to the vein at the tip of the cannula and remove the needle fully
Remove the cap from the needle and put this on the end of the cannula
Carefully dispose of the needle into the sharps box

## Slide 17: Technique
Check function by flushing with saline. If there is any resistance, if it causes any pain, or you notice any localized tissue swelling; immediately stop flushing, remove the cannula and start again
Apply the plaster to the cannula to fix it in place
Finally, ensure that the patient is comfortable and thank them

## Slide 18: Complications
Pain
Failure to access the vein
Blood stops flowing into the flashback chamber
Arterial puncture
Thrombophlebitis
Hypersensitivity reaction
Peripheral nerve palsy
Skin and soft tissue necrosis
  When some irritant solutions leak into the tissue e.g. chemotherapeutic agents
  More safely infused into a central vein

## Slide 19: Complications
Thrombophlebitis

## Slide 20: Complications
Thrombophlebitis
Hypersensitivity reaction
Peripheral nerve palsy

## Slide 21: Complications
Thrombophlebitis
Hypersensitivity reaction
Peripheral nerve palsy
Skin and soft tissue necrosis
  When some irritant solutions leak into the tissue e.g. chemotherapeutic agents
  More safely infused into a central vein